MQTT PROTOCOL
MQTT PROTOCOL
Lecturer: Dr. Bui Ha Duc
Dept. of Mechatronics
Email: ducbh@hcmute.edu.vn

---
Introduction to MQTT
Introduction to MQTT
- MQTT - Message Queuing Telemetry Transport
- MQTT was invented in 1999 by IBM as a Client Server publish/subscribe messaging transport protocol
- Advantages of MQTT:
  - Lightweight
  - Simple
  - Easy to implement
- MQTT is faster than HTTP’s.
- IBM used it internally, only release after version 3.1 in 2012.
- The current version is MQTT 5, released in 2019
[Speaker Notes: IBM used it internally, only release after version 3.1 in 2012. The current version is MQTT 5 released in 2019]

---
Client-Server Model
Client-Server Model
Traditional Client-Server architechture
[Speaker Notes: clients communicates directly with an endpoint/host Suitable for complex data packet, over-kill for simple data transmission. Like use truck as a taxi]

---
Publish/subscribe Model
Publish/subscribe Model
Publish/Subscribe Model
Broker (address ip:port)
filter all incoming messages
distribute them correctly to subscribers
Publisher - clients that send messages
Subscribers - clients that receive the messages
never contact each other directly
[Speaker Notes: they are not even aware that the other exists Data is only stored for a short time]

---
Publish/subscribe Model  (2)
Publish/subscribe Model
Publish/subscribe model has 3 features
  - Publisher and subscriber do not need to know each other (for example, no exchange of IP address and port).
  - Publisher and subscriber do not need to run at the same time.
  - Operations on both components do not need to be interrupted during publishing or receiving.
- MQTT uses topic filtering of messages
  - Topic is an UTF-8 string that the broker uses to filter messages for each connected client
  - Topic filters can contain wildcards: +, #

---
MQTT Topic
MQTT Topic
Topic consists of one or more topic levels, separated by “/”
A subscriber can use wild card to subscribe to multiple topic simultaneously

---
MQTT Message
MQTT Message
MQTT only has several types of message:
  - CONNECT: Used for clients to send connection requests to the broker
  - PUBLISH: Used by the client to publish messages to the broker
  - (UN)SUBSCRIBE: Used by the client to receive/stop receiving messages from the broker
  - ACKNOWLEDGEMENT: Used by receiver to confirm an action
    - CONNACK: Xác nhận kết nối.
    - PUBACK: Xác nhận rằng thông điệp PUBLISH đã được nhận.
    - PUBREC: Xác nhận rằng thông điệp PUBLISH đã được nhận (trong bước đầu của quá trình xác nhận QoS 2)
    - SUBACK: Xác nhận việc đăng ký (subscribe)
    - UNSUBACK : Xác nhận việc hủy đăng ký (unsubscribe) khỏi một chủ đề

---
MQTT Message (2)
MQTT Message
MQTT Message format:
(refer to this link for more detail: https://openlabpro.com/guide/mqtt-packet-format/ )

---
MQTT Message flow
MQTT Message flow
Client 1
Broker
CONNECT
CONNACK
Client 2
PUBLISH
PUBREC
SUBSCRIBE
SUBACK
Client 3
PUBLISH
PUBREC
UNSUBSCRIBE
UNSUBACK
MQTT is a command protocol, each command will be response by the receiver

---
MQTT Message flow - CONNECT
MQTT Message flow - CONNECT
Client 1
Broker
Server to client, connect acknowledgment
Connect message is sent by the client to the broker to initiate a connection
CONNECT
CONNACK
SUBSCRIBE
SUBACK
UNSUBSCRIBE
UNSUBACK
(refer to this link for more detail: https://www.hivemq.com/blog/mqtt-essentials-part-3-client-broker-connection-establishment/ )
[Speaker Notes: Both publishers and subscribers are MQTT clients. The client identifier (ClientId) identifies each MQTT client that connects to an MQTT broker. The broker uses the ClientId to identify the client and the current state of the client.Therefore, this Id should be unique per client and broker. In MQTT 3.1.1 you can send an empty ClientId, if you don’t need a state to be held by the broker. The empty ClientId results in a connection without any state. In this case, the clean session flag must be set to true or the broker will reject the connection. The clean session flag tells the broker whether the client wants to establish a persistent session or not. In a persistent session (CleanSession = false), the broker stores all subscriptions for the client and all missed messages for the client that subscribed with a Quality of Service (QoS) level 1 or 2. If the session is not persistent (CleanSession = true), the broker does not store anything for the client and purges all information from any previous persistent session.]

---
MQTT Message flow - PUBLISH
MQTT Message flow - PUBLISH
Broker
Client 2
PUBLISH
PUBACK
Client 3
PUBLISH
PUBREC

---
MQTT Message flow (2)
MQTT Message flow
Client 1
Broker
CONNECT
CONNACK
SUBSCRIBE
SUBACK
UNSUBSCRIBE
UNSUBACK

---
QoS – Quality of service
QoS – Quality of service

---
Setup MQTT Platform
Setup MQTT Platform
MQTT Broker:
  - Online Broker:
    - Paid: Amazon Azure, Google Cloud, IBM Cloud
    - “Free”: Eclipse, Mosquitto, Hivemq, emqx.io, Flespi…
  - On PC Broker: Mosquitto
    - https://mosquitto.org/
- MQTT Client library:
  - Eclipse Paho - https://www.eclipse.org/paho/
  - Notes: compile code C with “-lpaho-mqtt3c”
 e.g. gcc pub.c -o pub -lpaho-mqtt3c

---
Install Paho-MQTT
Install Paho-MQTT
sudo apt update
git clone https://github.com/eclipse/paho.mqtt.c.git
cd paho.mqtt.c
sudo apt install libssl-dev
make
sudo make install