## Slide 1: Low power Wide Area Network
Lecturer: Dr. Bui Ha Duc
Dept. of Mechatronics
Email: ducbh@hcmute.edu.vn

## Slide 2: Low power WAN
Wireless technologies adapted for long-range and battery-powered endpoints
Range > 2km
Types
  LoRaWAN
  Sigfox
  NB-IoT
  LTE
  …

## Slide 3: LoRaWAN
LoRa – Long Range
LoRA was developed by a French company named Cycleo in 2010
Semtech acquired Cycleo in May 2012
Lora used Chirp Spread Spectrum (CSS) modulation technology
Optimized for long-range, two-way communications and low power consumption
Nicolas Sornin

## Slide 4: LoRa Specifications
LoRa Alliance
https://lora-alliance.org/
LoRa Specifications:
  LoRa is deployed in a star-of-stars topology
  Data rate: range from 0.3 kbps to 50 kbps
  Packet size: is limited to 150 messages of 12 bytes per day
  Security: two layers of cryptography
    A unique 128-bit Network Session Key shared between the end-device and network server
    A unique 128-bit Application Session Key (AppSKey) shared end-to-end at the application level
LoRaWAN has three different classes of end-point devices

## Slide 5: LoRa Architecture
Gateways
  relay messages between end-devices and a central network server.
  The gateways are connected to the network server via standard IP connections and act as a transparent bridge

## Slide 6: LoRa Devices
LoRaWAN has three different classes of end-point devices
  Class A – Lowest power, bi-directional end-devices
    supported by all LoRaWAN end-devices
    fully asynchronous
    Can enter low-power sleep mode for as long as defined
  Class B – Bi-directional end-devices with deterministic downlink latency
    synchronized to the network using periodic beacons
    open downlink ‘ping slots’ at scheduled times
  Class C – Lowest latency, bi-directional end-devices
    reduces latency on the downlink by keeping the receiver of the end-device open at all times
    suitable for applications where continuous power is available
Notes: https://www.thethingsnetwork.org/docs/lorawan/classes/

## Slide 7: LoRa Devices

## Slide 8: LoRaWAN Layers
430MHz in Asia
Notes: Semtech is responsible for the PHY layer, while the LoRa Alliance handles the MAC layer and regional frequency bands

## Slide 9: LoRaWAN Layers
LoRa Physical layer
Semtech LoRa modulation is based on chirp spread spectrum modulation (CSS)
CSS trades a lower data rate for receiver sensitivity to significantly increase the communication distance
CSS allows demodulation below the noise floor
LoRa devices can receive on multiple channels in parallel

## Slide 10: LoRaWAN Layers
LoRa MAC layer
LoRaWAN endpoints are uniquely addressable through a variety of methods:
  global end device ID or DevEUI represented as an IEEE EUI-64 address.
  32-bit device address DevAddr